| Maintenance Task |  | Maintenance Interval |  |
| --- | --- | --- | --- |
|  | Weekly | Monthly | Quarterly | Half yearly | Yearly | 4 Years | 9 Years | Faculty list should work be required |
| Lubricate Plain Bearings | * |  |  |  |  |  |  | n/a |
| Check Lights throughout tower | * |  |  |  |  |  |  | n/a |
| Oil plain bearing pulleys (if applicable) |  | * | * | * | * |  |  | n/a |
| Check ropes |  | * | * | * | * |  |  | A |
| Check stays for looseness and cracks |  | * | * | * | * |  |  | A |
| Check for loose clapper/staples |  | * | * | * | * |  |  | n/a |
| Grease ball bearing pulleys (if applicable) |  |  | * | * | * |  |  | n/a |
| Clean and check runner boards/sliders |  |  | * | * | * |  |  | A |
| Grease clappers (if applicable) |  |  | * | * | * |  |  | n/a |
| Check tower roof drainage |  |  | * | * | * |  |  | R |
| Check tower for water ingress |  |  | * | * | * |  |  | R |
| Check pulleys for wear |  |  | * | * | * |  |  | A |
| Check “spider” cord |  |  | * | * | * |  |  | n/a |
| Clean ringing chamber |  |  | * | * | * |  |  | n/a |
| Check frame bolts |  |  |  | * | * |  |  | B |
| Check bearing bolts |  |  |  | * | * |  |  | B |
| Check for worn clapper bearings |  |  |  | * | * |  |  | A |
| Check for loose bell wheels |  |  |  | * | * |  |  | n/a |
| Check clock hammers and springs |  |  |  | * | * |  |  | F |
| Check chiming hammers |  |  |  | * | * |  |  | B |
| Check baring apparatus |  |  |  | * | * |  |  | F |
| Check for birds, etc |  |  |  | * | * |  |  | R |
| Check access stairs, ladders, access traps |  |  |  | * | * |  |  | R |
| Check safety of sound control system |  |  |  | * | * |  |  | n/a |
| Check rope chutes, bosses, guides |  |  |  |  | * |  |  | A |
| Check clock hammer wires |  |  |  |  | * |  |  | F |
| Check clock weights, wires and pulleys |  |  |  |  | * |  |  | F |
| Check tower and spire structure |  |  |  |  | * |  |  | R |
| Clean out dirt and rubbish |  |  |  |  | * |  |  | n/a |
| Treat rust outbreaks |  |  |  |  | * |  |  | A |
| Clean out Plain Bearings by lifting (if appropriate) |  |  |  |  |  | * |  | B |
| Treat woodwork with insecticide/fungicide |  |  |  |  |  | * |  | B |
| Repaint metal frames and fittings |  |  |  |  |  |  | * | A |
| Check security of fittings connected to simulator |  |  | * |  |  |  |  | n/a |
| Check that routine testing that all electrical equipment including heaters , simulators etc. has been undertaken |  |  |  |  |  | * |  | R |
| Test emergency lights (manufacturers specification) |  | * | * | * | * | * |  | A |

(Taken from ‘A Schedule of Regular Maintenance' published by the Central Council of Church Bell Ringers, with additions).

KEY

A	List A notification

B	List B Archdeacon’s permission

F	Faculty: the work is not on Lists A or B and may need a Faculty. Please contact the DAC Secretary.

R	Refer: the matter should be referred to the DAC and/or the church architect for advice. The work may require a Faculty.

n/a 	A matter of routine maintenance; no notification of permission required.

NB: ‘Checking’ does not include any work/replacements – before any work is carried out you must find out whether any permission is needed (List A, List B, or Faculty).